## Slide 1
FMEA Training

## Slide 2
Page 2
Purpose of the FMEA
Preventive costs to identify potential defects by FMEA’s are relatively low compared to in-house detection and correction of defects and even much lower than recovery costs in case defects are found by our Customers.
Identify and eliminate potential defects
Detection and correction of defects
Detection and correction EXTERNAL defects
Customer
Product development
Project planning
D-FMEA
Pre-
production
Production
Lifetime
Validation tests
Preventive costs
Warranty costs
P-FMEA
Cost of validation
Manufacturer / supplier

## Slide 3: FMEA
Purpose of the FMEA:
  Methodology that facilitates process improvement
  Identifies and eliminates concerns early in the development of a process or design
  Improve internal and external customer satisfaction
  Risk Management tool, focuses on prevention
  FMEA may be a customer requirement (likely contractual, Level 3 PPAP, ISO 9001)
Purpose of the FMEA
Page 3

## Slide 4: Learning FMEA, Training Objectives
Training Objectives:
To understand the use of Failure Modes and Effect Analysis(FMEA)
To learn the steps to developing FMEAs
To summarize the different types of FMEAs
To learn how to link the FMEA to other Process tools
Page 4

## Slide 5: FMEA, Summary
FMEA, a mathematical way to identify:
  failure modes, the ways in which a product or process can fail
  the Effects and Severity of a failure mode
  Potential causes of the failure mode
  the Occurrence of a failure mode
  the Detection of a failure mode
  the level of risk (Risk Priority Number)
  actions that should be taken to reduce the RPN
Page 5
  RPN = Severity X Occurrence X Detection

## Slide 6: Benefits
FMEA, Inputs
Page 6
Inputs might include other tools such as:
D-FMEA (Part and Assembly level) Defines VOC
  Customer requirements
  CTQ Flow down analysis
  Quality Function Deployment (House Of Quality)
  Risk assessments
P-FMEA (Process level) Delivers VOC
  Process flowchart
  Sequence Of Events
  Process Tooling
  Poka-Yoke list

## Slide 7: FMEA, Application Examples
There are several situations where an FMEA is the optimal tool to identify risk:
Process-FMEA:
  Introducing a new process
  Reviewing existing processes after modifications
  Introduce new Part Numbers on an existing Production Line
Design-FMEA:
  Introducing a new Design, Part, Sub Assembly or Assembly
  Use an existing Design for another application
  Reviewing existing Designs after modifications
Page 7

## Slide 8: What Is A Failure Mode?
A Failure Mode is:
  The way in which the component, subassembly, product or process could fail to perform its intended function
  Failure modes may be the result of previous operations or may cause next operations to fail
  Things that could go wrong INTERNALLY:
    Warehouse
    Production Process
  Things that could go wrong EXTERNALLY:
    Supplier Location
    Final Customer
Page 8

## Slide 9: When to Conduct an FMEA
When to Conduct an FMEA?
Early in the New Product Introduction (A-Build) complete for B build.
When new systems, products, and processes are being designed
When existing designs or processes are being changed, FMEA’s to be updated
When process improvements are made due to Corrective Action Requests
Page 9

## Slide 10: History of FMEA
History of FMEA:
First used in the 1960’s in the Aerospace industry during the Apollo missions
In 1974, the Navy developed MIL-STD-1629 regarding the use of FMEA
In the late 1970’s, the automotive industry was driven by liability costs to use FMEA
Later, the automotive industry saw the advantages of using this tool to reduce risks related to poor quality (QS-9000, VDA and ISO-TS 16949 standard)
Page 10

## Slide 11: History of FMEA, Case Study
Page 11
Case Study, what could have been avoided using FMEA
AubieSat-1 was the first ever, 4-inch Cube Satellite to be accepted by NASA for launch.
It was launched into space 28 th October 2011 from Vandenberg Air Force Base in California on a NASA-sponsored Delta II rocket.

## Slide 12: History of FMEA, Case Study
Page 12
What was the failure mode?
Once the satellite was deployed:
the team had problems making contact with the satellite
One of the 2 antennae failed to deploy
The signal transmitter at the control center did not have enough power to communicate with the satellite
How was it solved?
The team used another signal transmitter from an earlier flight which had enough power to enable communication
Lessons learned:
Plan for errors!
The use of an FMEA most likely had avoided the malfunction involving people from the earlier flight
Teamwork!
The collaboration relationship between teams enabled the team to use the alternative equipment. Without it, the mission could have failed.
Why Do I Care?
First Time Right, Calculated Risk, Rights Team will safe resources!

## Slide 13: Types of FMEAs
Design FMEA
  Analyzes product design before release to production, with a focus on product function
  Analyzes systems and subsystems in early concept and design stages
Process FMEA
  Used to analyze manufacturing and assembly processes before they are implemented
Page 13

## Slide 14: FMEA: A Team Tool
A team approach is necessary, see example AubieSat-1
communication problems could have been avoided by involving a practical experienced team!
Team should be led by the Right person, Design, Manufacturing or Quality Engineer, etc…familiar with FMEA
The following Team members should be considered:
  Design Engineers
  Process Engineers
  Supply Chain Engineers
  Line Design Engineers
  Suppliers
  Operators
  Practical Experts
Page 14

## Slide 15: The FMEA Form
Identify failure modes and their effects
Identify causes of the failure modes
and controls
Prioritize
Determine and assess actions
Page 15

## Slide 16: FMEA Procedure
For each process input determine the ways in which the input can go wrong (failure mode)
2. For each failure mode, determine effects
  Select a Severity level for each effect
3. Identify potential causes of each failure mode
  Select an Occurrence level for each cause
4. List current controls for each cause
  Select a Detection level for each cause
Page 16
  RPN = Severity X Occurrence X Detection

## Slide 17: FMEA Procedure (Cont.)
5. Calculate the Risk Priority Number (RPN)
6. Develop recommended actions, assign responsible persons, and take actions
  Give priority to high RPNs
  MUST look at highest severity
7. Assign the predicted Severity, Occurrence, and Detection levels and compare RPNs (before and after risk reduction)
Page 17

## Slide 18: Rating Scales
Preferred Scales are1-10
Adjust Occurence scales to reality figures for your company
Page 18
Severity:
1 = Not Severe, 10 = Very Severe
Occurrence:
1 = Not Likely, 10 = Very Likely
Detection:
1 = Easy to Detect, 10 = Not easy to Detect

## Slide 19: The FMEA Form
Identify failure modes and their effects
Identify causes of the failure modes
and controls
Prioritize
Determine and assess actions
A Closer Look
Page 19

## Slide 20
Risk Assessment with FMEA
Page 20
Notes: Key point is “Team”. It’s not uncommon for a single person being responsible to update a document. When this occurs, we are not taking it seriously enough.

## Slide 21
How capable are we of detecting the failure mode with our current controls?
Document current process controls!
Potential for occurrence!
Identify potential root causes of failure mode!
Determine Severity of failure mode!
Identify consequences of that failure!
Identify failure modes at each process step!
Risk Assessment with FMEA
Risk Priority Number (RPN).
Highest # equals Highest Risk!
Severity x Occurrence x Detectability = RPN
Use Like Pareto Chart to identify what items to address first.
Page 21
Notes: Key point is “Team”. It’s not uncommon for a single person being responsible to update a document. When this occurs, we are not taking it seriously enough.

## Slide 22
Page 22
Risk Assessment with FMEA
Severity
Occurrence
Detection
Notes: Highlight some of the key differences such as the Extreme Severity (without warning = 10 & with warning =9)

## Slide 23
CASTING ATTACH TORQUE
OVER TORQUE
UNDER TORQUE
CROSS THREAD
CASTING FRACTURE
CASTING SEPARATION
CASTING SEPARATION
10
9
9
TORQUE WRENCH NOT CONTROLLED
TORQUE WRENCH NOT USED/ CONTROLLED
NO LEAD IN ON BOLT THREAD
4
DC TORQUE WRENCH USED / LINKED TO OMS
3
120
ADD TORQUE ALARM AND CALIBRATION AT START UP.
JENNY TONE
10
2
20
1
Page 23
Risk Assessment with FMEA
Notes: Without warning is the key explanation with a brake casting fracture. Need to explain that’s why we need further action as the occurrence is still present at 1 in 2000.

## Slide 24: Risk Priority Number (RPN)
RPN is the product of the severity, occurrence, and detection scores
Severity
Occurrence
Detection
RPN
X
X
=
Page 24

## Slide 25: FMEA, 10 Steps Checklist
Page 25
10 Steps to Conduct a PFMEA
1
Review the process—Use a process flowchart to identify each process component
Brainstorm potential failure modes—Review existing documentation and data for clues
List potential effects of failure—There may be more than one for each failure
Assign Severity rankings—Based on the severity of the consequences of failure
Assign Occurrence rankings—Based on how frequently the cause of the failure is likely to occur
Assign Detection rankings—Based on the chances the failure will be detected prior to the customer finding it
Calculate the RPN—Severity X Occurrence X Detection
Develop the action plan—Define who will do what by when
Take action—Implement the improvements identified by your PFMEA team
Calculate the resulting RPN—Re-evaluate each of the potential failures once improvements have been made and determine the impact of the improvements